## Slide 1: Machine-Level Programming V: Advanced Topics 15-213 / 18-213: Introduction to Computer Systems 9th Lecture, Sep. 24, 2013
Instructors:
Randy Bryant, Dave O’Hallaron, and Greg Kesden

## Slide 2: Today
Structures
  Alignment
Unions
Memory Layout
Buffer Overflow
  Vulnerability
  Protection

## Slide 3: Structures & Alignment
Unaligned Data
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8
c
i[0]
i[1]
v
p
p+1
p+5
p+9
p+17
struct S1 {
char c;
int i[2];
double v;
} *p;

## Slide 4: Alignment Principles
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
  Required on some machines; advised on IA32
    treated differently by IA32 Linux, x86-64 Linux, and Windows!
Motivation for Aligning Data
  Memory accessed by (aligned) chunks of 4 or 8 bytes (system dependent)
    Inefficient to load or store datum that spans quad word boundaries
    Virtual memory very tricky when datum spans 2 pages
Compiler
  Inserts gaps in structure to ensure correct alignment of fields

## Slide 5: Specific Cases of Alignment (IA32)
1 byte: char, …
  no restrictions on address
2 bytes: short, …
  lowest 1 bit of address must be 02
4 bytes: int, float, char *, …
  lowest 2 bits of address must be 002
8 bytes: double, …
  Windows (and most other OS’s & instruction sets):
    lowest 3 bits of address must be 0002
  Linux:
    lowest 2 bits of address must be 002
    i.e., treated the same as a 4-byte primitive data type
12 bytes: long double
  Windows (GCC), Linux:
    lowest 2 bits of address must be 002
    i.e., treated the same as a 4-byte primitive data type

## Slide 6: Specific Cases of Alignment (x86-64)
1 byte: char, …
  no restrictions on address
2 bytes: short, …
  lowest 1 bit of address must be 02
4 bytes: int, float, …
  lowest 2 bits of address must be 002
8 bytes: double, long, char *, …
  lowest 3 bits of address must be 0002
16 bytes: long double (GCC on Linux or Windows)
  lowest 4 bits of address must be 00002

## Slide 7: Satisfying Alignment with Structures
struct S1 {
char c;
int i[2];
double v;
} *p;
Within structure:
  Must satisfy each element’s alignment requirement
Overall structure placement
  Each structure has alignment requirement K
    K = Largest alignment of any element
  Initial address & structure length must be multiples of K
Example (under Windows or x86-64):
  K = 8, due to double element
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8

## Slide 8: Different Alignment Conventions
Windows, x86-64
  K = 8, due to double element
IA32 Linux
  K = 4; double treated like a 4-byte data type
struct S1 {
char c;
int i[2];
double v;
} *p;
 | c | 3 bytes |  |  | i[0] |  |  |  | i[1] |  |  |  | 4 bytes |  |  |  | v |  |  |  |  |  |  |  | 
p+0 |  |  |  | p+4 |  |  |  | p+8 |  |  |  |  |  |  |  | p+16 |  |  |  |  |  |  |  | p+24 | 
 | c | 3 bytes |  |  | i[0] |  |  |  | i[1] |  |  |  | v |  |  |  |  |  |  |  |  |  |  | 
p+0 |  |  |  | p+4 |  |  |  | p+8 |  |  |  | p+12 |  |  |  |  |  |  | p+20 |  |  |  |  | 

## Slide 9: Meeting Overall Alignment Requirement (Windows, x86-64)
For largest alignment requirement K
Overall structure must be multiple of K
struct S2 {
double v;
int i[2];
char c;
} *p;
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
p+0 |  |  |  |  |  |  | p+8 |  |  |  |  |  |  |  | p+16 |  |  |  |  |  |  |  | p+24 | 
Multiple of K=8

## Slide 10: Arrays of Structures (Windows, x86-64)
Overall structure length multiple of K
Satisfy alignment requirement for every element
struct S2 {
double v;
int i[2];
char c;
} a[10];
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
a+24 |  |  |  |  |  |  | a+32 |  |  |  |  |  |  |  | a+40 |  |  |  |  |  |  |  | a+48 | 
 | a[0] |  |  |  |  | a[1] |  |  |  |  | a[2] |  |  |  |  | • • • |  |  |  |  |  | 
a+0 |  |  |  |  | a+24 |  |  |  |  | a+48 |  |  |  |  | a+72 |  |  |  |  |  |  | 

## Slide 11: Meeting Overall Alignment Requirement (IA32 Linux)
For largest alignment requirement K
Overall structure must be multiple of K
  Up to maximum of K=4
struct S2 {
double v;
int i[2];
char c;
} *p;
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 3 bytes |  |  | 
p+0 |  |  |  |  |  |  | p+8 |  |  |  |  |  |  |  | p+16 |  |  |  | p+20 | 
Multiple of K=4

## Slide 12: Arrays of Structures (IA32 Linux)
Overall structure length multiple of K
Satisfy alignment requirement for every element
struct S2 {
double v;
int i[2];
char c;
} a[10];
 | a[0] |  |  |  |  | a[1] |  |  |  |  | a[2] |  |  |  |  | • • • |  |  |  |  |  | 
a+0 |  |  |  |  | a+20 |  |  |  |  | a+40 |  |  |  |  | a+60 |  |  |  |  |  |  | 
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 3 bytes |  |  | 
a+0 |  |  |  |  |  |  | a+8 |  |  |  |  |  |  |  | a+16 |  |  |  | a+20 | 

## Slide 13: Accessing Array Elements
Compute array offset 12*idx
  sizeof(S3), including alignment spacers
Element j is at offset 8 within structure
Assembler gives offset a+8
  Resolved during linking
struct S3 {
short i;
float v;
short j;
} a[10];
short get_j(int idx)
{
return a[idx].j;
}
# %eax = idx
leal (%eax,%eax,2),%eax # 3*idx
movswl a+8(,%eax,4),%eax
 | a[0] |  |  |  |  | • • • |  |  |  | a[idx] |  |  |  | • • |  |  | • |  |  | 
a+0 |  |  |  |  | a+12 |  |  |  | a+12*idx |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | i | 2 bytes |  | v |  |  | j | 2 bytes |  |  | 
 |  |  |  | a+12*idx |  |  |  |  |  | a+12*idx+8 |  |  |  |  | 

## Slide 14: Saving Space
Put large data types first
Effect (K=4)
struct S4 {
char c;
int i;
char d;
} *p;
struct S5 {
int i;
char c;
char d;
} *p;
c
i
3 bytes
d
3 bytes
c
i
d
2 bytes

## Slide 15: Today
Structures
  Alignment
Unions
Memory Layout
Buffer Overflow
  Vulnerability
  Protection

## Slide 16: Union Allocation
Allocate according to largest element
Can only use one field at a time
union U1 {
char c;
int i[2];
double v;
} *up;
struct S1 {
char c;
int i[2];
double v;
} *sp;
 | c | 3 bytes |  |  | i[0] |  |  |  | i[1] |  |  |  | 4 bytes |  |  | v |  |  |  |  |  | 
sp+0 |  |  |  | sp+4 |  |  |  | sp+8 |  |  |  |  |  |  | sp+16 |  |  |  |  |  | sp+24 | 
 | c |  |  |  |  |  |  |  | 
 | i[0] |  |  |  | i[1] |  |  |  | 
 | v |  |  |  |  |  |  |  | 
up+0 |  |  | up+4 |  |  |  |  | up+8 | 
(Windows or x86-64)

## Slide 17: Using Union to Access Bit Patterns
typedef union {
float f;
unsigned u;
} bit_float_t;
float bit2float(unsigned u) {
bit_float_t arg;
arg.u = u;
return arg.f;
}
unsigned float2bit(float f) {
bit_float_t arg;
arg.f = f;
return arg.u;
}
Same as (float) u ?
Same as (unsigned) f ?
 | u |  |  |  | 
 | f |  |  |  | 
0 |  |  |  | 4 | 

## Slide 18: Byte Ordering Revisited
Idea
  Short/long/quad words stored in memory as 2/4/8 consecutive bytes
  Which byte is most (least) significant?
  Can cause problems when exchanging binary data between machines
Big Endian
  Most significant byte has lowest address
  Sparc
Little Endian
  Least significant byte has lowest address
  Intel x86, ARM Android and IOS
Bi Endian
  Can be configured either way
  ARM

## Slide 19: Byte Ordering Example
union {
unsigned char c[8];
unsigned short s[4];
unsigned int i[2];
unsigned long l[1];
} dw;
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
32-bit
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
64-bit

## Slide 20: Byte Ordering Example (Cont).
int j;
for (j = 0; j < 8; j++)
dw.c[j] = 0xf0 + j;
printf("Characters 0-7 == [0x%x,0x%x,0x%x,0x%x,0x%x,0x%x,0x%x,0x%x]\n",
dw.c[0], dw.c[1], dw.c[2], dw.c[3],
dw.c[4], dw.c[5], dw.c[6], dw.c[7]);
printf("Shorts 0-3 == [0x%x,0x%x,0x%x,0x%x]\n",
dw.s[0], dw.s[1], dw.s[2], dw.s[3]);
printf("Ints 0-1 == [0x%x,0x%x]\n",
dw.i[0], dw.i[1]);
printf("Long 0 == [0x%lx]\n",
dw.l[0]);

## Slide 21: Byte Ordering on IA32
Little Endian
Characters 0-7 == [0xf0,0xf1,0xf2,0xf3,0xf4,0xf5,0xf6,0xf7]
Shorts 0-3 == [0xf1f0,0xf3f2,0xf5f4,0xf7f6]
Ints 0-1 == [0xf3f2f1f0,0xf7f6f5f4]
Long 0 == [0xf3f2f1f0]
Output:
f0 | f1 | f2 | f3 | f4 | f5 | f6 | f7
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
LSB
MSB
LSB
MSB
Print

## Slide 22: Byte Ordering on Sun
Big Endian
Characters 0-7 == [0xf0,0xf1,0xf2,0xf3,0xf4,0xf5,0xf6,0xf7]
Shorts 0-3 == [0xf0f1,0xf2f3,0xf4f5,0xf6f7]
Ints 0-1 == [0xf0f1f2f3,0xf4f5f6f7]
Long 0 == [0xf0f1f2f3]
Output on Sun:
f0 | f1 | f2 | f3 | f4 | f5 | f6 | f7
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
MSB
LSB
MSB
LSB
Print

## Slide 23: Byte Ordering on x86-64
Little Endian
Characters 0-7 == [0xf0,0xf1,0xf2,0xf3,0xf4,0xf5,0xf6,0xf7]
Shorts 0-3 == [0xf1f0,0xf3f2,0xf5f4,0xf7f6]
Ints 0-1 == [0xf3f2f1f0,0xf7f6f5f4]
Long 0 == [0xf7f6f5f4f3f2f1f0]
Output on x86-64:
f0 | f1 | f2 | f3 | f4 | f5 | f6 | f7
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
LSB
MSB
Print

## Slide 24: Summary
Arrays in C
  Contiguous allocation of memory
  Aligned to satisfy every element’s alignment requirement
    IA32 Linux unusual in only requiring 4-byte alignment for 8-byte data
  Pointer to first element
  No bounds checking
Structures
  Allocate bytes in order declared
  Pad in middle and at end to satisfy alignment
Unions
  Overlay declarations
  Way to circumvent type system

## Slide 25: Today
Structures
  Alignment
Unions
Memory Layout
Buffer Overflow
  Vulnerability
  Protection

## Slide 26: IA32 Linux Memory Layout
Stack
  Runtime stack (8MB limit)
  E. g., local variables
Heap
  Dynamically allocated storage
  When call malloc(), calloc(), new()
Data
  Statically allocated data
  E.g., global vars, static vars, strings
Text
  Executable machine instructions
  Read-only
Upper 2 hex digits = 8 bits of address
FF
00
Stack
Text
Data
Heap
08
8MB
not drawn to scale

## Slide 27: Memory Allocation Example
char big_array[1<<24]; /* 16 MB */
char huge_array[1<<28]; /* 256 MB */
int beyond;
char *p1, *p2, *p3, *p4;
int useless() { return 0; }
int main()
{
p1 = malloc(1 <<28); /* 256 MB */
p2 = malloc(1 << 8); /* 256 B */
p3 = malloc(1 <<28); /* 256 MB */
p4 = malloc(1 << 8); /* 256 B */
/* Some print statements ... */
}
FF
00
Stack
Text
Data
Heap
08
not drawn to scale
Where does everything go?

## Slide 28: IA32 Example Addresses
$esp 0xffffbcd0
p3 0x65586008
p1 0x55585008
p4 0x1904a110
p2 0x1904a008
&p2 0x18049760
&beyond 0x08049744
big_array 0x18049780
huge_array 0x08049760
main() 0x080483c6
useless() 0x08049744
final malloc() 0x006be166
address range ~232
FF
00
Stack
Text
Data
Heap
08
80
not drawn to scale
malloc() is dynamically linked
address determined at runtime

## Slide 29: x86-64 Example Addresses
$rsp 0x00007ffffff8d1f8
p3 0x00002aaabaadd010
p1 0x00002aaaaaadc010
p4 0x0000000011501120
p2 0x0000000011501010
&p2 0x0000000010500a60
&beyond 0x0000000000500a44
big_array 0x0000000010500a80
huge_array 0x0000000000500a50
main() 0x0000000000400510
useless() 0x0000000000400500
final malloc() 0x000000386ae6a170
address range ~247
00007F
000000
Stack
Text
Data
Heap
000030
not drawn to scale
malloc() is dynamically linked
address determined at runtime

## Slide 30: Today
Structures
  Alignment
Unions
Memory Layout
Buffer Overflow
  Vulnerability
  Protection

## Slide 31: Internet Worm and IM War
November, 1988
  Internet Worm attacks thousands of Internet hosts.
  How did it happen?

## Slide 32: Internet Worm and IM War
July, 1999
  Microsoft launches MSN Messenger (instant messaging system).
  Messenger clients can access popular AOL Instant Messaging Service (AIM) servers
AIM
server
AIM
client
AIM
client
MSN
client
MSN
server

## Slide 33: Internet Worm and IM War (cont.)
August 1999
  Mysteriously, Messenger clients can no longer access AIM servers.
  Microsoft and AOL begin the IM war:
    AOL changes server to disallow Messenger clients
    Microsoft makes changes to clients to defeat AOL changes.
    At least 13 such skirmishes.
  How did it happen?

## Slide 34: Internet Worm and IM War (cont.)
The Internet Worm and AOL/Microsoft War were both based on stack buffer overflow exploits!
    many library functions do not check argument sizes.
    allows target buffers to overflow.

## Slide 35: String Library Code
Implementation of Unix function gets()
  No way to specify limit on number of characters to read
Similar problems with other library functions
  strcpy, strcat: Copy strings of arbitrary length
  scanf, fscanf, sscanf, when given %s conversion specification
/* Get string from stdin */
char *gets(char *dest) { int c = getchar();
char *p = dest;
while (c != EOF && c != '\n') {
*p++ = c;
c = getchar();
}
*p = '\0';
return dest;
}

## Slide 36: Vulnerable Buffer Code
void call_echo() {
echo();
}
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ gets(buf); puts(buf); }
unix>./bufdemo
Type a string:0123456789a
0123456789a
unix>./bufdemo
Type a string:0123456789ab
Segmentation Fault

## Slide 37: Buffer Overflow Disassembly
080485c3 <echo>:
80485c3: 55 push %ebp
80485c4: 89 e5 mov %esp,%ebp
80485c6: 53 push %ebx
80485c7: 83 ec 24 sub $0x24,%esp
80485ca: 8d 5d f4 lea -0xc(%ebp),%ebx
80485cd: 89 1c 24 mov %ebx,(%esp)
80485d0: e8 9e ff ff ff call 8048573 <gets>
80485d5: 89 1c 24 mov %ebx,(%esp)
80485d8: e8 2f fe ff ff call 804840c <puts@plt>
80485dd: 83 c4 24 add $0x24,%esp
80485e0: 5b pop %ebx
80485e1: 5d pop %ebp
80485e2: c3 ret
. . .
80485e9: e8 d5 ff ff ff call 80485c3 <echo>
80485ee: c9 leave
80485ef: c3 ret
call_echo:
echo:

## Slide 38: Buffer Overflow Stack
echo:
pushl %ebp # Save %ebp on stack
movl %esp, %ebp
pushl %ebx # Save %ebx
subl $36, %esp # Allocate stack space
leal -12(%ebp),%ebx # Compute buf as %ebp-12
movl %ebx, (%esp) # Push buf on stack
call gets # Call gets
. . .
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ gets(buf); puts(buf); }
Return Address
Saved %ebp
%ebp
Stack Frame
for main
Stack Frame
for echo
[3]
[2]
[1]
[0]
buf
Before call to gets
Saved %ebx
4 bytes unused

## Slide 39: Buffer Overflow Stack Example
unix> gdb bufdemo
(gdb) break echo
Breakpoint 1 at 0x80485c9
(gdb) run
Breakpoint 1, 0x80485c9 in echo ()
(gdb) print /x $ebp
$1 = 0xffffd248
(gdb) print /x *(unsigned *)$ebp
$2 = 0xffffd258
(gdb) print /x *((unsigned *)$ebp + 1)
$3 = 0x80485ee
(gdb) print /x *((unsigned *)$ebp - 1)
$4 = 0x2c3ff4
80485e9: e8 d5 ff ff ff call 80485c3 <echo>
80485ee: c9 leave
0xffffd248
Return Address
Saved %ebp
%ebp
Stack Frame
for main
Stack Frame
for echo
[3]
[2]
[1]
[0]
buf
Before call to gets
Saved %ebx
4 bytes unused
%ebp
buf
Stack Frame
for main
Stack Frame
for echo
xx
xx
xx
xx
Before call to gets
00
2c
3f
f4
ff
ff
d2
58
08
04
85
ee
xx
xx
xx
xx
Saved %ebx
return address
0xffffd258

## Slide 40: Buffer Overflow Example #1
Overflow buf, and corrupt %ebx,
but no adverse effects
Input 0123456789a
%ebp
buf
Stack Frame
for main
Stack Frame
for echo
xx
xx
xx
xx
Before call to gets
00
2c
3f
f4
ff
ff
d2
58
08
04
85
ee
xx
xx
xx
xx
Saved %ebx
return address
0xffffd258
%ebp
buf
Stack Frame
for main
Stack Frame
for echo
33
32
31
30
00
61
39
38
ff
ff
d2
58
08
04
85
ee
37
36
35
34
Saved %ebx
return address
0xffffd258

## Slide 41: Buffer Overflow Example #2
Base pointer
corrupted!
. . .
80485e9: e8 d5 ff ff ff call 80485c3 <echo>
80485ee: c9 leave # Set %ebp to bad value
80485ef: c3 ret
Input 0123456789ab
%ebp
buf
Stack Frame
for main
Stack Frame
for echo
xx
xx
xx
xx
Before call to gets
00
2c
3f
f4
ff
ff
d2
58
08
04
85
ee
xx
xx
xx
xx
Saved %ebx
return address
0xffffd258
%ebp
buf
Stack Frame
for main
Stack Frame
for echo
33
32
31
30
62
61
39
38
ff
ff
d2
00
08
04
85
ee
37
36
35
34
Saved %ebx
return address
0xffffd200

## Slide 42: Buffer Overflow Example #3
Return address
corrupted!
. . .
80485e9: e8 d5 ff ff ff call 80485c3 <echo>
80485ee: c9 leave # Desired return point
Input 0123456789abcdef
%ebp
buf
Stack Frame
for main
Stack Frame
for echo
xx
xx
xx
xx
Before call to gets
00
2c
3f
f4
ff
ff
d2
58
08
04
85
ee
xx
xx
xx
xx
Saved %ebx
return address
0xffffd258
%ebp
buf
Stack Frame
for main
Stack Frame
for echo
33
32
31
30
62
61
39
38
66
65
64
63
08
04
85
00
37
36
35
34
Saved %ebx
return address
0xffffd200

## Slide 43: Buffer Overflow Example #4
Can we trick program into calling a different function?
Idea: Alter return address on stack
0804861e <gotcha>:
804861e: 55 push %ebp
. . .
%ebp
buf
Stack Frame
for main
Stack Frame
for echo
xx
xx
xx
xx
Before call to gets
00
2c
3f
f4
ff
ff
d2
58
08
04
85
ee
xx
xx
xx
xx
Saved %ebx
return address
0xffffd258
void gotcha() {
printf(
"This function should not get called!\n”
);
}

## Slide 44: Buffer Overflow Example #4
Alter return address on stack
Exploit string:
  00 00 00 00 00 00 00 00 (8X)
  00 00 00 00 00 00 00 00 (8X)
  1e 86 04 08 (Little Endian)
Must supply as raw bytes
  E.g., via tool hex2raw
  See Buffer Lab
0804861e <gotcha>:
804861e: 55 push %ebp
. . .
%ebp
buf
Before call to gets
Stack Frame
for main
Stack Frame
for echo
00
00
00
00
00
00
00
00
00
00
00
00
08
04
86
1e
00
00
00
00
Saved %ebx
return address
0xffffd258
00

## Slide 45: Malicious Use of Buffer Overflow
Input string contains byte representation of executable code
Overwrite return address A with address of buffer B
When bar() executes ret, will jump to exploit code
int bar() {
char buf[64];
gets(buf);
...
return ...;
}
void foo(){
bar();
...
}
Stack after call to gets()
B
return
address
A
foo stack frame
bar stack frame
B
exploit
code
pad
data written
by gets()

## Slide 46: Exploits Based on Buffer Overflows
Buffer overflow bugs allow remote machines to execute arbitrary code on victim machines
Internet worm
  Early versions of the finger server (fingerd) used gets() to read the argument sent by the client:
    finger droh@cs.cmu.edu
  Worm attacked fingerd server by sending phony argument:
    finger “exploit-code padding new-return-address”
    exploit code: executed a root shell on the victim machine with a direct TCP connection to the attacker.

## Slide 47: Exploits Based on Buffer Overflows
Buffer overflow bugs allow remote machines to execute arbitrary code on victim machines
IM War
  AOL exploited existing buffer overflow bug in AIM clients
  exploit code: returned 4-byte signature (the bytes at some location in the AIM client) to server.
  When Microsoft changed code to match signature, AOL changed signature location.

## Slide 48
Date: Wed, 11 Aug 1999 11:30:57 -0700 (PDT)
From: Phil Bucking <philbucking@yahoo.com>
Subject: AOL exploiting buffer overrun bug in their own software!
To: rms@pharlap.com
Mr. Smith,
I am writing you because I have discovered something that I think you
might find interesting because you are an Internet security expert with
experience in this area. I have also tried to contact AOL but received
no response.
I am a developer who has been working on a revolutionary new instant
messaging client that should be released later this year.
...
It appears that the AIM client has a buffer overrun bug. By itself
this might not be the end of the world, as MS surely has had its share.
But AOL is now *exploiting their own buffer overrun bug* to help in
its efforts to block MS Instant Messenger.
....
Since you have significant credibility with the press I hope that you
can use this information to help inform people that behind AOL's
friendly exterior they are nefariously compromising peoples' security.
Sincerely,
Phil Bucking
Founder, Bucking Consulting
philbucking@yahoo.com
It was later determined that this email originated from within Microsoft!

## Slide 49: Avoiding Overflow Vulnerability
Use library routines that limit string lengths
  fgets instead of gets
  strncpy instead of strcpy
  Don’t use scanf with %s conversion specification
    Use fgets to read the string
    Or use %ns where n is a suitable integer
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ fgets(buf, 4, stdin); puts(buf); }

## Slide 50: System-Level Protections
unix> gdb bufdemo
(gdb) break echo
(gdb) run
(gdb) print /x $ebp
$1 = 0xffffc638
(gdb) run
(gdb) print /x $ebp
$2 = 0xffffbb08
(gdb) run
(gdb) print /x $ebp
$3 = 0xffffc6a8
Randomized stack offsets
  At start of program, allocate random amount of space on stack
  Makes it difficult for hacker to predict beginning of inserted code
  Currently disabled on shark machines
Nonexecutable code segments
  In traditional x86, can mark region of memory as either “read-only” or “writeable”
    Can execute anything readable
  X86-64 added explicit “execute” permission

## Slide 51: Stack Canaries
Idea
  Place special value (“canary”) on stack just beyond buffer
  Check for corruption before exiting function
GCC Implementation
  -fstack-protector
  -fstack-protector-all
unix>./bufdemo-protected
Type a string:123
123
unix>./bufdemo-protected
Type a string:1234
*** stack smashing detected ***

## Slide 52: Protected Buffer Disassembly
804864b: 55 push %ebp
804864c: 89 e5 mov %esp,%ebp
804864e: 53 push %ebx
804864f: 83 ec 24 sub $0x24,%esp
8048652: 65 a1 14 00 00 00 mov %gs:0x14,%eax
8048658: 89 45 f4 mov %eax,-0xc(%ebp)
804865b: 31 c0 xor %eax,%eax
804865d: 8d 5d f0 lea -0x10(%ebp),%ebx
8048660: 89 1c 24 mov %ebx,(%esp)
8048663: e8 77 ff ff ff call 80485df <gets>
8048668: 89 1c 24 mov %ebx,(%esp)
804866b: e8 f0 fd ff ff call 8048460 <puts@plt>
8048670: 8b 45 f4 mov -0xc(%ebp),%eax
8048673: 65 33 05 14 00 00 00 xor %gs:0x14,%eax
804867a: 74 05 je 8048681 <echo+0x36>
804867c: e8 cf fd ff ff call 8048450 <...fail...>
8048681: 83 c4 24 add $0x24,%esp
8048684: 5b pop %ebx
8048685: 5d pop %ebp
8048686: c3 ret
echo:

## Slide 53: Setting Up Canary
echo:
. . .
movl %gs:20, %eax # Get canary
movl %eax, -12(%ebp) # Put on stack
xorl %eax, %eax # Erase canary
. . .
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ gets(buf); puts(buf); }
Return Address
Saved %ebp
%ebp
Stack Frame
for main
Stack Frame
for echo
[3]
[2]
[1]
[0]
buf
Before call to gets
Saved %ebx
Canary

## Slide 54: Checking Canary
echo:
. . .
movl -12(%ebp), %eax # Retrieve from stack
xorl %gs:20, %eax # Compare with Canary
je .L24 # Same: skip ahead
call _stack_chk_fail # ERROR
.L24:
. . .
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ gets(buf); puts(buf); }
Return Address
Saved %ebp
%ebp
Stack Frame
for main
Stack Frame
for echo
[3]
[2]
[1]
[0]
buf
Before call to gets
Saved %ebx
Canary

## Slide 55: Canary Example
(gdb) break echo
(gdb) run
(gdb) stepi 3
(gdb) print /x *((unsigned *) $ebp - 3)
$1 = dafccb23
Return Address
Saved %ebp
%ebp
Stack Frame
for main
Stack Frame
for echo
[3]
[2]
[1]
[0]
buf
Before call to gets
Saved %ebx
da
fc
cb
23
Return Address
Saved %ebp
%ebp
Stack Frame
for main
Stack Frame
for echo
buf
Input 1234
Saved %ebx
da
fc
cb
00
34
33
32
31
Canary corrupted

## Slide 56: Worms and Viruses
Worm: A program that
  Can run by itself
  Can propagate a fully working version of itself to other computers
Virus: Code that
  Add itself to other programs
  Cannot run independently
Both are (usually) designed to spread among computers and to wreak havoc

## Slide 57: Summary
Structures
  Alignment
Unions
Memory Layout
Buffer Overflow
  Vulnerability
  Protection