## Slide 1: Cache Memories 15-213: Introduction to Computer Systems 11th Lecture, Oct. 1, 2013
Instructors:
Randy Bryant, Dave O’Hallaron, and Greg Kesden

## Slide 2: Today
Cache memory organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 3: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 4: An Example Memory Hierarchy
Registers
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
Remote secondary storage
(tapes, distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
costlier
per byte

## Slide 5: General Cache Concept
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 6: Many types of caches
Examples
  Hardware: L1, L2, L3 cache memories, TLBs, …
  Software: Virtual memory, FS buffers, Web browser caches, …
Hardware cache memories
  Significant impact on program performance
  Topic of today’s lecture

## Slide 7: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware
  Hold frequently accessed blocks of main memory
CPU looks first for data in cache, then in main memory
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memory

## Slide 8: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 9: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 10: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 11: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag

## Slide 12: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
If tag doesn’t match: old line is evicted and replaced

## Slide 13: Direct-Mapped Cache Simulation
M=16 bytes (4-bit addresses), B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3

## Slide 14: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 15: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 16: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 17: 2-Way Set Associative Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 18: What about writes?
Multiple copies of data exist:
  L1, L2, L3, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes straight to memory, does not load into cache)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 19: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Block size: 64 bytes for all caches.

## Slide 20: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    1-2 clock cycle for L1
    5-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 21: Lets think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 22: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories

## Slide 23: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 24: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 25: Memory Mountain Test Function
/* The test function */
void test(int elems, int stride) {
int i, result = 0;
volatile int sink;
for (i = 0; i < elems; i += stride)
result += data[i];
sink = result; /* So compiler doesn't optimize away the loop */
}
/* Run test(elems, stride) and return read throughput (MB/s) */
double run(int size, int stride, double Mhz)
{
double cycles;
int elems = size / sizeof(int);
test(elems, stride); /* warm up the cache */
cycles = fcyc2(test, elems, stride, 0); /* call test(elems,stride) */
return (size / stride) / (cycles / Mhz); /* convert cycles to MB/s */
}

## Slide 26: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip

## Slide 27: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip
Slopes of
spatial
locality

## Slide 28: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip
Slopes of
spatial
locality
Ridges of
temporal
locality

## Slide 29: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 30: Miss Rate Analysis for Matrix Multiply
Assume:
  Line size = 32B (big enough for four 64-bit words)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j
=
x

## Slide 31: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register

## Slide 32: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > 4 bytes, exploit spatial locality
    miss rate = 4 bytes / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    miss rate = 1 (i.e. 100%)

## Slide 33: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 34: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 35: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25

## Slide 36: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25

## Slide 37: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0

## Slide 38: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0

## Slide 39: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 40: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50.0 | 100.0 | 150.0 | 200.0 | 250.0 | 300.0 | 350.0 | 400.0 | 450.0 | 500.0 | 550.0 | 600.0 | 650.0 | 700.0 | 750.0
jki | 6.4 | 6.87 | 4.14 | 5.53 | 10.93 | 33.23 | 49.43 | 51.49 | 52.06 | 52.06 | 52.07 | 52.09 | 52.12 | 52.17 | 52.2
kji | 6.4 | 6.82 | 4.01 | 5.33 | 11.04 | 33.21 | 49.42 | 51.5 | 52.07 | 52.08 | 52.09 | 52.1 | 52.14 | 52.19 | 52.23
ijk | 5.31 | 6.35 | 6.29 | 3.7 | 3.72 | 3.71 | 3.72 | 3.83 | 4.6 | 7.74 | 11.71 | 16.54 | 20.57 | 23.85 | 23.86
jik | 5.4 | 6.23 | 3.64 | 3.71 | 3.61 | 3.6 | 3.63 | 3.74 | 4.64 | 7.57 | 11.62 | 16.44 | 20.44 | 23.68 | 23.66
kij | 4.37 | 5.36 | 3.23 | 3.32 | 3.29 | 3.24 | 3.2 | 3.17 | 3.16 | 3.14 | 3.13 | 3.12 | 3.1 | 3.1 | 3.08
ikj | 3.58 | 5.31 | 3.19 | 3.18 | 3.15 | 3.12 | 3.1 | 3.1 | 3.11 | 3.09 | 3.07 | 3.06 | 3.02 | 3.02 | 3.01
jki / kji
ijk / jik
kij / ikj

## Slide 41: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 42: Example: Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n+j] += a[i*n + k]*b[k*n + j];
}

## Slide 43: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide

## Slide 44: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3
n
*
=
8 wide

## Slide 45: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=B)
for (j = 0; j < n; j+=B)
for (k = 0; k < n; k+=B)
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i++)
for (j1 = j; j1 < j+B; j++)
for (k1 = k; k1 < k+B; k++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
c
+
Block size B x B

## Slide 46: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
First (block) iteration:
  B2/8 misses for each block
  2n/B * B2/8 = nB/4 (omitting matrix c)
  Afterwards in cache (schematic)
*
=
*
=
Block size B x B
n/B blocks

## Slide 47: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Second (block) iteration:
  Same as first iteration
  2n/B * B2/8 = nB/4
Total misses:
  nB/4 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 48: Blocking Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
Suggest largest possible block size B, but limit 3B2 < C!
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly

## Slide 49: Cache Summary
Cache memories can have significant performance impact
You can write your programs to exploit this!