## Slide 1
14-513
18-613

## Slide 2: Machine-Level Programming II: Control 15-213/18-213/14-513/15-513/18-613: Introduction to Computer Systems 6th Lecture, September 12, 2019

## Slide 3: Today
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 4: Recall: ISA = Assembly/Machine Code View
CPU
Programmer-Visible State
  PC: Program counter
    Address of next instruction
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic or logical operation
    Used for conditional branching
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes
  Memory
    Byte addressable array
    Code and user data
    Stack to support procedures

## Slide 5: Recall: Turning C into Object Code
text
text
binary
binary
Compiler (gcc –Og -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc –Og p1.c p2.c -o p
    Use basic optimizations (-Og) [New to recent versions of GCC]
    Put resulting binary in file p

## Slide 6: Recall: Move & Arithmetic Operations
Some Two Operand Instructions:
  Format Computation
    movq Src,Dest
    leaq Src,Dest
    addq Src,Dest
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    salq Src,Dest Dest = Dest << Src Also called shlq
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    shrq Src,Dest Dest = Dest >> Src Logical
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Dest = Src (Src can be $const)
Dest = address computed by expression Src
Dest = Dest + Src

## Slide 7: Recall: Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 8: Processor State (x86-64, Partial)
Information about currently executing program
  Temporary data ( %rax, … )
  Location of runtime stack ( %rsp )
  Location of current code control point ( %rip, … )
  Status of recent tests ( CF, ZF, SF, OF )
%rip
Registers
Current stack top
Instruction pointer
CF
ZF
SF
OF
Condition codes
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 9: Condition Codes (Implicit Setting)
Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Implicitly set (as side effect) of arithmetic operations
  Example: addq Src,Dest ↔ t = a+b
  CF set if carry/borrow out from most significant bit (unsigned overflow)
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by leaq instruction

## Slide 10: ZF set when
000000000000…00000000000

## Slide 11: SF set when
yxxxxxxxxxxxx...
yxxxxxxxxxxxx...
+
1xxxxxxxxxxxx...
For signed arithmetic, this reports when result is a negative number

## Slide 12: CF set when
1xxxxxxxxxxxx...
1xxxxxxxxxxxx...
+
xxxxxxxxxxxxx...
1
For unsigned arithmetic, this reports overflow
0xxxxxxxxxxxx...
1xxxxxxxxxxxx...
-
1xxxxxxxxxxxx...
1
Carry
Borrow

## Slide 13: OF set when
yxxxxxxxxxxxx...
yxxxxxxxxxxxx...
+
zxxxxxxxxxxxx...
z = ~y
For signed arithmetic, this reports overflow
  (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
a
b
t

## Slide 14: Condition Codes (Explicit Setting: Compare)
Explicit Setting by Compare Instruction
  cmpq Src2, Src1
  cmpq b,a like computing a-b without setting destination
  CF set if carry/borrow out from most significant bit (used for unsigned comparisons)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)

## Slide 15: Condition Codes (Explicit Setting: Test)
Explicit Setting by Test instruction
  testq Src2, Src1
    testq b,a like computing a&b without setting destination
  Sets condition codes based on value of Src1 & Src2
  Useful to have one of the operands be a mask
  ZF set when a&b == 0
  SF set when a&b < 0
Very often:
testq %rax,%rax

## Slide 16: Condition Codes (Explicit Reading: Set)
Explicit Reading by Set Instructions
  setX Dest: Set low-order byte of destination Dest to 0 or 1 based on combinations of condition codes
  Does not alter remaining 7 bytes of Dest
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (signed)
setge | ~(SF^OF) | Greater or Equal (signed)
setl | SF^OF | Less (signed)
setle | (SF^OF)¦ZF | Less or Equal (signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 17: Example: setl (Signed <)
Condition: SF^OF
SF | OF | SF ^ OF | Implication
0 | 0 | 0 | 
1 | 0 | 1 | 
0 | 1 | 1 | 
1 | 1 | 0 | 
1xxxxxxxxxxxx...
0xxxxxxxxxxxx...
-
0xxxxxxxxxxxx...
a
b
t
negative overflow case
No overflow, so SF implies not <
No overflow, so SF implies <
Overflow, so SF implies negative overflow, i.e. <
Overflow, so SF implies positive overflow, i.e. not <

## Slide 18: x86-64 Integer Registers
%rsp
  Can reference low-order byte
%al
%bl
%cl
%dl
%sil
%dil
%spl
%bpl
%r8b
%r9b
%r10b
%r11b
%r12b
%r13b
%r14b
%r15b
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 19: Explicit Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when >
  movzbl %al, %eax # Zero rest of %rax
ret
SetX Instructions:
  Set single byte based on combination of condition codes
One of addressable byte registers
  Does not alter remaining bytes
  Typically use movzbl to finish job
    32-bit instructions also set upper 32 bits to 0
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 20: Explicit Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when >
  movzbl %al, %eax # Zero rest of %rax
ret
SetX Instructions:
  Set single byte based on combination of condition codes
One of addressable byte registers
  Does not alter remaining bytes
  Typically use movzbl to finish job
    32-bit instructions also set upper 32 bits to 0
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
Beware weirdness movzbl (and others)
movzbl %al, %eax
%eax
%al
%rax
0x000000
%al
%rax
0x00000000
0x000000
%al
Zapped to all 0’s

## Slide 21: Today
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 22: Jumping
jX Instructions
  Jump to different part of code depending on condition codes
  Implicit reading of condition codes
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (signed)
jge | ~(SF^OF) | Greater or Equal (signed)
jl | SF^OF | Less (signed)
jle | (SF^OF)¦ZF | Less or Equal (signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 23: Conditional Branch Example (Old Style)
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
absdiff:
cmpq %rsi, %rdi # x:y
jle .L4
movq %rdi, %rax
subq %rsi, %rax
ret
.L4: # x <= y
movq %rsi, %rax
subq %rdi, %rax
ret
Generation
  shark> gcc –Og -S –fno-if-conversion control.c
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
Get to this shortly

## Slide 24: Expressing with Goto Code
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
C allows goto statement
Jump to position designated by label
long absdiff_j
(long x, long y)
{
long result;
int ntest = x <= y;
if (ntest) goto Else;
result = x-y;
goto Done;
Else:
result = y-x;
Done:
return result;
}

## Slide 25: General Conditional Expression Translation (Using Branches)
C Code
val = Test ? Then_Expr : Else_Expr;
Goto Version
ntest = !Test;
if (ntest) goto Else;
val = Then_Expr;
goto Done;
Else:
val = Else_Expr;
Done:
. . .
  Create separate code regions for then & else expressions
  Execute appropriate one
val = x>y ? x-y : y-x;

## Slide 26: Using Conditional Moves
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
result = Then_Expr;
eval = Else_Expr;
nt = !Test;
if (nt) result = eval;
return result;
Conditional Move Instructions
  Instruction supports:
    if (Test) Dest  Src
  Supported in post-1995 x86 processors
  GCC tries to use them
    But, only when known to be safe
Why?
  Branches are very disruptive to instruction flow through pipelines
  Conditional moves do not require control transfer

## Slide 27: Conditional Move Example
absdiff:
movq %rdi, %rax # x
subq %rsi, %rax # result = x-y
movq %rsi, %rdx
subq %rdi, %rdx # eval = y-x
cmpq %rsi, %rdi # x:y
cmovle %rdx, %rax # if <=, result = eval
ret
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
When is
this bad?

## Slide 28: Bad Cases for Conditional Move
Expensive Computations
Both values get computed
Only makes sense when computations are very simple
val = Test(x) ? Hard1(x) : Hard2(x);
Risky Computations
Both values get computed
May have undesirable effects
val = p ? *p : 0;
Computations with side effects
Both values get computed
Must be side-effect free
val = x > 0 ? x*=7 : x+=3;
Bad Performance
Unsafe
Illegal

## Slide 29: Exercise
xorq %rax, %rax
subq $1, %rax
cmpq $2, %rax
setl %al
movzblq %al, %eax
%rax | SF | CF | OF | ZF
0x0000 0000 0000 0000 | 0 | 0 | 0 | 1
0xFFFF FFFF FFFF FFFF | 1 | 1 | 0 | 0
0xFFFF FFFF FFFF FFFF | 1 | 0 | 0 | 0
0xFFFF FFFF FFFF FF01 | 1 | 0 | 0 | 0
0x0000 0000 0000 0001 | 1 | 0 | 0 | 0
cmpq b,a like computing a-b w/o setting dest
CF set if carry/borrow out from most significant bit (used for unsigned comparisons)
ZF set if a == b
SF set if (a-b) < 0 (as signed)
OF set if two’s-complement (signed) overflow
Note: setl and movzblq do not modify condition codes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (signed)
setge | ~(SF^OF) | Greater or Equal (signed)
setl | SF^OF | Less (signed)
setle | (SF^OF)¦ZF | Less or Equal (signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 30: Exercise
xorq %rax, %rax
subq $1, %rax
cmpq $2, %rax
setl %al
movzblq %al, %eax
%rax | SF | CF | OF | ZF
0x0000 0000 0000 0000 | 0 | 0 | 0 | 1
0xFFFF FFFF FFFF FFFF | 1 | 1 | 0 | 0
0xFFFF FFFF FFFF FFFF | 1 | 0 | 0 | 0
0xFFFF FFFF FFFF FF01 | 1 | 0 | 0 | 0
0x0000 0000 0000 0001 | 1 | 0 | 0 | 0
cmpq b,a like computing a-b w/o setting dest
CF set if carry/borrow out from most significant bit (used for unsigned comparisons)
ZF set if a == b
SF set if (a-b) < 0 (as signed)
OF set if two’s-complement (signed) overflow
Note: setl and movzblq do not modify condition codes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (signed)
setge | ~(SF^OF) | Greater or Equal (signed)
setl | SF^OF | Less (signed)
setle | (SF^OF)¦ZF | Less or Equal (signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 31: Today
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 32: “Do-While” Loop Example
C Code
long pcount_do
(unsigned long x) {
long result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
Goto Version
long pcount_goto
(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Count number of 1’s in argument x (“popcount”)
Use conditional branch to either continue looping or to exit loop

## Slide 33: “Do-While” Loop Compilation
movl $0, %eax # result = 0
.L2: # loop:
movq %rdi, %rdx
andl $1, %edx # t = x & 0x1
addq %rdx, %rax # result += t
shrq %rdi # x >>= 1
jne .L2 # if(x) goto loop
rep; ret
long pcount_goto
(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Register | Use(s)
%rdi | Argument x
%rax | result

## Slide 34: Quiz Time!
Check out:
https://canvas.cmu.edu/courses/10968

## Slide 35: General “Do-While” Translation
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
Body:
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 36: General “While” Translation #1
While version
while (Test)
Body
“Jump-to-middle” translation
Used with -Og
Goto Version
goto test;
loop:
Body
test:
if (Test)
goto loop;
done:

## Slide 37: While Loop Example #1
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Jump to Middle Version
long pcount_goto_jtm
(unsigned long x) {
long result = 0;
goto test;
loop:
result += x & 0x1;
x >>= 1;
test:
if(x) goto loop;
return result;
}
Compare to do-while version of function
Initial goto starts loop at test

## Slide 38: General “While” Translation #2
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
“Do-while” conversion
Used with –O1
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 39: While Loop Example #2
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Do-While Version
long pcount_goto_dw
(unsigned long x) {
long result = 0;
if (!x) goto done;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
done:
return result;
}
Initial conditional guards entrance to loop
Compare to do-while version of function
  Removes jump to middle. When is this good or bad?
Notes: If more often not entering loop, then skip unnecessary unconditional jump to the middle, which just evaluates to done.

## Slide 40: “For” Loop Form
for (Init; Test; Update )
Body
General Form
#define WSIZE 8*sizeof(int)
long pcount_for
(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 41: “For” Loop  While Loop
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version

## Slide 42: For-While Conversion
long pcount_for_while
(unsigned long x)
{
size_t i;
long result = 0;
i = 0;
while (i < WSIZE)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
i++;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 43: “For” Loop Do-While Conversion
C Code
Initial test can be optimized away – why?
long pcount_for
(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
return result;
}
Goto Version
long pcount_for_goto_dw
(unsigned long x) {
size_t i;
long result = 0;
i = 0;
if (!(i < WSIZE))
goto done;
loop:
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
i++;
if (i < WSIZE)
goto loop;
done:
return result;
}
Init
!Test
Body
Update
Test
Notes: Can optimize away when initial condition is known. Ie, compiler knows that i=0 b/c it is in the for loop, compiler knows bound if it is not variable, hence, can cut.

## Slide 44: Today
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 45: Switch Statement Example
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
long my_switch
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 46: Jump Table Structure
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
jtab:
goto *JTab[x];
switch(x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Translation (Extended C)
Jump Table
Jump Targets

## Slide 47: Switch Statement Example
Setup
long my_switch(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
my_switch:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8
jmp *.L4(,%rdi,8)
What range of values takes default?
Note that w not initialized here
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value
Notes: Cmpq 6 rdi  go to default if above all case values
W not initialized until it is sure to be used.

## Slide 48: Switch Statement Example
long my_switch(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
Indirect jump
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Setup
Setup
my_switch:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8 # use default
jmp *.L4(,%rdi,8) # goto *Jtab[x]
Notes: *.L4(,rdi,8) is L4 + rdi * addrsize  go to *Jtab[x], with x in rdi

## Slide 49: Assembly Setup Explanation
Table Structure
  Each target requires 8 bytes
  Base address at .L4
Jumping
  Direct: jmp .L8
  Jump target is denoted by label .L8
  Indirect: jmp *.L4(,%rdi,8)
  Start of jump table: .L4
  Must scale by factor of 8 (addresses are 8 bytes)
  Fetch target from effective Address .L4 + x*8
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6

## Slide 50: Jump Table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}

## Slide 51: Code Blocks (x == 1)
.L3:
movq %rsi, %rax # y
imulq %rdx, %rax # y*z
ret
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 52: Handling Fall-Through
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
case 3:
w = 1;
case 2:
w = y/z;
goto merge;
merge:
w += z;

## Slide 53: Code Blocks (x == 2, x == 3)
.L5: # Case 2
movq %rsi, %rax
cqto # sign extend
# rax to rdx:rax
idivq %rcx # y/z
jmp .L6 # goto merge
.L9: # Case 3
movl $1, %eax # w = 1
.L6: # merge:
addq %rcx, %rax # w += z
ret
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rcx | z
%rax | Return value

## Slide 54: Code Blocks (x == 5, x == 6, default)
.L7: # Case 5,6
movl $1, %eax # w = 1
subq %rdx, %rax # w -= z
ret
.L8: # Default:
movl $2, %eax # 2
ret
switch(x) {
. . .
case 5: // .L7
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 55: Summarizing
C Control
  if-then-else
  do-while
  while, for
  switch
Assembler Control
  Conditional jump
  Conditional move
  Indirect jump (via jump tables)
  Compiler generates code sequence to implement more complex control
Standard Techniques
  Loops converted to do-while or jump-to-middle form
  Large switch statements use jump tables
  Sparse switch statements may use decision trees (if-elseif-elseif-else)

## Slide 56: Summary
Today
  Control: Condition codes
  Conditional branches & conditional moves
  Loops
  Switch statements
Next Time
  Stack
  Call / return
  Procedure call discipline

## Slide 57: Finding Jump Table in Binary
00000000004005e0 <switch_eg>:
4005e0: 48 89 d1 mov %rdx,%rcx
4005e3: 48 83 ff 06 cmp $0x6,%rdi
4005e7: 77 2b ja 400614 <switch_eg+0x34>
4005e9: ff 24 fd f0 07 40 00 jmpq *0x4007f0(,%rdi,8)
4005f0: 48 89 f0 mov %rsi,%rax
4005f3: 48 0f af c2 imul %rdx,%rax
4005f7: c3 retq
4005f8: 48 89 f0 mov %rsi,%rax
4005fb: 48 99 cqto
4005fd: 48 f7 f9 idiv %rcx
400600: eb 05 jmp 400607 <switch_eg+0x27>
400602: b8 01 00 00 00 mov $0x1,%eax
400607: 48 01 c8 add %rcx,%rax
40060a: c3 retq
40060b: b8 01 00 00 00 mov $0x1,%eax
400610: 48 29 d0 sub %rdx,%rax
400613: c3 retq
400614: b8 02 00 00 00 mov $0x2,%eax
400619: c3 retq

## Slide 58: Finding Jump Table in Binary (cont.)
00000000004005e0 <switch_eg>:
. . .
4005e9: ff 24 fd f0 07 40 00 jmpq *0x4007f0(,%rdi,8)
. . .
% gdb switch
(gdb) x /8xg 0x4007f0
0x4007f0: 0x0000000000400614 0x00000000004005f0
0x400800: 0x00000000004005f8 0x0000000000400602
0x400810: 0x0000000000400614 0x000000000040060b
0x400820: 0x000000000040060b 0x2c646c25203d2078
(gdb)

## Slide 59: Finding Jump Table in Binary (cont.)
% gdb switch
(gdb) x /8xg 0x4007f0
0x4007f0: 0x0000000000400614 0x00000000004005f0
0x400800: 0x00000000004005f8 0x0000000000400602
0x400810: 0x0000000000400614 0x000000000040060b
0x400820: 0x000000000040060b 0x2c646c25203d2078
. . .
4005f0: 48 89 f0 mov %rsi,%rax
4005f3: 48 0f af c2 imul %rdx,%rax
4005f7: c3 retq
4005f8: 48 89 f0 mov %rsi,%rax
4005fb: 48 99 cqto
4005fd: 48 f7 f9 idiv %rcx
400600: eb 05 jmp 400607 <switch_eg+0x27>
400602: b8 01 00 00 00 mov $0x1,%eax
400607: 48 01 c8 add %rcx,%rax
40060a: c3 retq
40060b: b8 01 00 00 00 mov $0x1,%eax
400610: 48 29 d0 sub %rdx,%rax
400613: c3 retq
400614: b8 02 00 00 00 mov $0x2,%eax
400619: c3 retq